Architectural Specification

QMI Security Solutions

1661 Glenlake Ave, Itasca IL 60143

800-446-2500  www.qmiusa.com

For Fixed Type Rectangular or Shaped
Window and Door opening Protection and Security Screen

Section 08660 Security Screens-Fixed and Shaped

PAGE ONE OF THREE

1.0 GENERAL

1.1 DESCRIPTION
Provide permanently installed heavy-duty Aluminum Fixed Hurricane, Energy Saving and Security Screens.

Hurricane, Energy Saving and Security Protection Screens shall provide continuous and easy window viewing as well as provide air ventilation when required. Shutters or Screens that prohibit easy viewing and air ventilation shall not be accepted. Perforated or Expanded Metal Shutters/Screens, Solid Panel Shutters, Accordion, Electric or Pull down Shutters shall not be accepted under this specification section. 

1.2 SCOPE
All aluminum screen frames with stainless steel wire mesh units covered under this specification shall be of the fixed type, consisting of a main frame and wire cloth. No plastic, steel or galvanized steel parts shall be accepted. Screens shall be permanently installed. Screens with hinges and locking systems shall not be accepted.

2.0 MATERIAL

2.1 MAINFRAME 
Screen mainframe shall be hollow extruded aluminum alloy minimum 6005 T5 with a minimum 2 3/8” face, 1 1/4” thick and .062 wall thickness. Mainframe shall have a minimum tensile strength of 38,000 lbs. per square inch. 

2.2 WIRE LOCK RETAINERS
Screen wire lock retainers shall be of solid extruded aluminum alloy of 6005 T5 with a minimum wall thickness of .062 and having a minimum tensile strength of 38,000 pounds per square inch.

2.3 MULLIONS
Screen frame mullions shall not be accepted or approved.

2.4 HARDWARE
All fasteners, screws, and other miscellaneous fastening and hardware components shall be of aluminum, stainless steel or salt sprayed coated galvanized steel providing maximum strength for security and weather protection. No plastic parts shall be accepted.

3.0 CONSTRUCTION

ASSEMBLY: All screen units shall be assembled with corner gusset construction in a secure workmanlike manner to perform as herein specified to assure a complete constructed unit. All screens shall be constructed with one continuous piece of stainless steel wire.

PAGE TWO OF THREE

3.1 MAINFRAME
All corners of screen mainframe shall be miter cut, fitted together with a .125 thick, 2” aluminum architectural angles. Each mainframe corner will be secured with a minimum of four aluminum pop rivets. No exposed fasteners on the interior or exterior of mainframe are permitted. 

3.2 SCREEN WIRE
Screen wire material is high-tensile 304 stainless steel with mesh count to be 12 x 12 strands per inch at 0.028 diameter. Screen wire mesh shall be one continuous piece with 1” wide, 90 degree bends on all four sides.

3.4 WIRE LOCK RETAINERS
Screen Wire shall be placed into mainframe receptor channels and wire lock retainer shall be miter cut, fitted, and placed over 1” wire angles on all four sides, fastened to screen mainframe with #12 x 3/4" stainless steel or salt sprayed coated steel screws 4” on centers.

4.0 HARDWARE

4.1 FASTENERS
All fasteners, screws, and other miscellaneous fastening and hardware components shall be of aluminum, stainless steel or salt sprayed coated galvanized steel providing maximum strength for security and weather protection. No plastic parts shall be accepted.

5.0 FINISH

5.1 CLEANING / PAINTING
The exposed surfaces of all aluminum members, screen material, and screws shall be clean and free from serious surface blemishes. Screen wire to be corrosion pre-treated and powder coated with standard Kynar Powder Coat, electrostatic applied, and baked on, black only. Frame and sash profiles to be standard Kynar Powder Coated, electrostatic applied, and baked on. Standard colors are White and Bronze, with custom colors available upon customer request. Finish shall be selected by owner, architect or authorized agent. Samples of the standard or custom finishes shall be provided upon request. Warranty on the paint finish shall be guaranteed for a minimum of 10 years.          

6.0 INSTALLATION

6.1 INSTALLATION
Where face mounting of screen frame is not applicable, inside mounting of the screen frame with a tubing system  or L angles shall apply.

- Security installation:  recommended spacing 6” from corners and fastener spacing sufficient to firmly attach screen frame to substrate.  Fasteners should be appropriate and sufficient for substrate.  Fasteners must be attached to structure.  Attachment to window or door frames is unacceptable.

7.0 CLEAN UP and DAMAGES

7.1 CLEAN UP
The contractor shall be responsible for clean up and removal of any debris caused by the screen installation.

7.2 DAMAGES
The contractor shall be responsible for any property or tenant damages due to negligence during the screen installation.

PAGE THREE OF THREE

8.0 MEASUREMENTS & SITE VISIT

Awarded contractor shall be responsible for site visit, exact field measurements and quantities prior to and after submittal of their bid.

9.0 QUALITY ASSURANCE

9.1 GUARANTEE
All installation shall be guaranteed for a period of one (1) year. All screen hardware and shall be guaranteed for a period of one (1) year from the date of installation.

9.2 CERTIFICATIONS/REPORTS. As a minimum, stainless steel wire cloth 12 x 12 x .028 diameter shall be used. 

9.3 PRODUCT APPROVALS
Prior product approval is required to be eligible for bidding. At a minimum of 10 days prior to the bid date, a full sized sample with literature, and shop drawings at 1/8” scale must be submitted to the Architect, Owner or Authorized Agent for review and acceptance as well as other documents, certifications and requirements in this specification.

10.0 DEFINITION STATEMENT
The requirements in this specification are based on research and intended to provide the very best product based on manufacturer’s model type, experience, testing reports, certifications and salt air performances. 



END OF SECTION